## Slide 1
Jaypee Institute of Information Technology, Noida, U.P.
Electronics & Communication Engineering Discipline

## Slide 2
Essentials of an Instrument
Permanent Magnet Moving Coil (PMMC) Instruments
Voltmeter
Ammeter
Ohmmeter
Meter Sensitivity (Ohms-Per-Volt Rating)
Loading Effect
Multimeter
Cathode Ray Oscilloscope: Construction, Working and Applications
Function Generators
Jaypee Institute of Information Technology
Electrical Instruments

## Slide 3
Essentials of an Instrument
Jaypee Institute of Information Technology
The instrument used for measuring the physical and electrical quantities is known as the measuring instrument.
Measurement means the comparison between the two quantities of the same unit.
The magnitude of one of the quantity is unknown, and it is compared with the predefined value.
The measuring instrument categorized into three types
Mechanical Instrument
Electrical Instrument
Electronic Instrument

## Slide 4
Permanent Magnet Moving Coil (PMMC) Instruments
Jaypee Institute of Information Technology
1. Mechanical instruments:- They are very reliable for static and stable conditions. The disadvantage is they are unable to respond rapidly to measurement of dynamic and transient conditions.
2. Electrical instruments:- Electrical methods of indicating the output of detectors are more rapid than mechanical methods.
  The electrical system normally depends upon a mechanical meter movement as indicating device. The electrical instrument is used for measuring electrical quantities likes current, voltage, power, etc.
  The ammeter, voltmeter, wattmeter are the examples of the electrical measuring instrument.
  The ammeter measures the current in amps; voltmeter measures voltage and Wattmeter are used for measuring the power.
3. Electronic instruments:- These instruments have very fast response as compared to the electrical and mechanical instrument.
For example a cathode ray oscilloscope (CRO) is capable to follow dynamic and transient changes of the order of few nano seconds (10-9 sec).

## Slide 5
Major quantity is measured in all instrument
Jaypee Institute of Information Technology
Accuracy: It is the ability of the instrument to measure the accurate value. In other words, it is the closeness of the measured value to a standard or true value. Example
Input T1 = 50 K
Input T2 = 50 K
Input T3 = 50 K
Precision: The term precision means two or more values of the measurements are closed to each other.
  The high precision means the result of the measurements are consistent or the repeated values of the reading are obtained.
  The low precision means the value of the measurement varies.
  But it is not necessary that the highly precise reading gives the accurate result.
Instrument1
Output T1 = 46 K
Instrument2
Instrument3
Output T2 = 47 K
Output T3 = 49.5 K

## Slide 6
Major quantity is measured in all instrument
Jaypee Institute of Information Technology
Example:
Input F = 10 N
Input F = 10 N
Input F = 10 N
Sensitivity : It is the smallest amount of difference in quantity that will change an instrument's reading.
Example:
Input F1 = 10 N
F2 = 05 N
F3 = 0.4 N
Resolution is the smallest unit of measurement that can be indicated by an instrument.
Instrument1
Output F = 6 N, 7 N, 8 N, 9 N
Instrument2
Instrument3
Output F = 7 N, 7 N, 7 N, 7 N
Output F = 9 N, 7 N, 8 N, 9 N
Instrument
Output F1 = 0 N
F2 = 0 N
F3 = Not Zero