## Slide 1: Ohm for AC
An AC circuit is made up with components.
  Power source
  Resistors
  Capacitor
  Inductors
Kirchhoff’s laws apply just like DC.
R
C
L

## Slide 2: Inductor Current
The voltage across an inductor vL = Ldi/ dt and at the moment of switching (transient, t = 0) the voltage required to induce a change in the inductor current is ∞, hence the inductor current can not change instantly which gives the statement: iL(0−) = iL(0+)
In the steady state condition in DC circuits (i.e. when t → ∞), the inductor acts as a short circuit. (VL = Ldi/dt : the inductor current is constant and the voltage across it =0, hence s.c.)

## Slide 3: Capacitor Voltage
The current flowing into the capacitor iC = C dvC/dt and at the moment of switching (transient, t = 0) the current required to induce a change in the capacitor voltage is ∞, hence the capacitor voltage can not change instantly which gives the statement: vC(0−) = vC(0+)
In the steady state condition in DC circuits (i.e. when t → ∞), the capacitor acts as an open circuit. (iC = C dvC/dt the capacitor is fully charged and the current flowing through it =0, hence o.c.)

## Slide 4: Transients
The time-varying currents and voltages resulting from the sudden application of sources, usually due to switching, are called transients. By writing circuit equations, we obtain integrodifferential equations.

## Slide 5: DC Steady State Response
The steps in determining the forced response
for RLC circuits with dc sources are:
1. Replace capacitances with open circuits.
2. Replace inductances with short circuits.
3. Solve the remaining circuit.

## Slide 6: First-Order Circuits
A circuit that contains only sources, resistors and an inductor is called an RL circuit.
A circuit that contains only sources, resistors and a capacitor is called an RC circuit.
RL and RC circuits are called first-order circuits because their voltages and currents are described by first-order differential equations.
–
+
vs
L
R
–
+
vs
C
R
i
i

## Slide 7
  In steady state (t = Infinity), an inductor behaves like a short circuit
  In steady state (t = Infinity), a capacitor behaves like an open circuit

## Slide 8
The natural response of an RL or RC circuit is its behavior (i.e., current and voltage) when stored energy in the inductor or capacitor is released to the resistive part of the network (containing no independent sources).
The step response of an RL or RC circuit is its behavior when a voltage or current source step is applied to the circuit

## Slide 9: Natural Response of an RL Circuit
Consider the following circuit, for which the switch is closed for t < 0, and then opened at t = 0. Find v for t>0
  Notation:
    0– is used to denote the time just prior to switching
    0+ is used to denote the time immediately after switching
The current flowing in the inductor at t = 0– is Io
L
Ro
R
Io
t = 0
i
+
v
–

## Slide 10: Solving for the Current (t  0)
For t > 0, the circuit reduces to
Applying KVL to the LR circuit yields first-order D.E.:
L di/dt + iR = 0
L[sI(s) – I(0-)] +RI(s) = 0
I(s) = I(0-)*L/(R+Ls)
Solution:
L
Ro
R
Io
i
+
v
–
= I0e-(R/L)t

## Slide 11: Solving for the Voltage (t > 0)
L
Ro
R
Io
+
v
–
Re
I
iR
t
v
t
t
L
R
o
=
=
>
-
)
(
0,
for
)
/
(
11

## Slide 12: Time Constant t
In the example, we found that
Define the time constant
  At t = t, the current has reduced to 1/e (~0.37) of its initial value.
  At t = 5t, the current has reduced to less than 1% of its initial value.
(sec)

## Slide 13: Capacitors and Stored Charge
Current doesn’t really “flow through” a capacitor. No electrons can go through the insulator.
But, we say that current flows through a capacitor. What we mean is that positive charge collects on one plate and leaves the other.
A capacitor stores charge.
When a capacitor stores charge, it has nonzero voltage. In this case, we say the capacitor is “charged”. A capacitor with zero voltage has no charge differential, and we say it is “discharged”.

## Slide 14: Capacitors in circuits
If you have a circuit with capacitors, you can use KVL and KCL, nodal analysis, etc.
The voltage across the capacitor is related to the current through it by a differential equation instead of Ohm’s law.

## Slide 15: CAPACITORS
capacitance is defined by
C
i(t)
| (
V
+

15

## Slide 16: Charging a Capacitor with a constant current
C
i
| (
V(t)
+

time
voltage
16

## Slide 17: Voltage vs time for an RC discharge
Voltage
Time

## Slide 18: Natural Response of an RC Circuit
Consider the following circuit, for which the switch is closed for t < 0, and then opened at t = 0:
  Notation:
    0– is used to denote the time just prior to switching
    0+ is used to denote the time immediately after switching
The voltage on the capacitor at t = 0– is Vo as cap is open circuit
C
Ro
R
Vo
t = 0
+

+
v
–

## Slide 19: Solving for the Voltage (t  0)
For t > 0, the circuit reduces to
Applying KCL to the RC circuit:
V + RCdv/dt = 0
V(s) + RC[sV(s) – Vo] = 0
Solving:
+
v
–
C
Ro
R
Vo
+

i
19

## Slide 20: Solving for the Current (t > 0)
Note that the current changes abruptly:
+
v
–
C
Ro
R
Vo
+

i
20

## Slide 21: Time Constant t
In the example, we found that
Define the time constant
  At t = t, the voltage has reduced to 1/e (~0.37) of its initial value.
  At t = 5t, the voltage has reduced to less than 1% of its initial value.
(sec)

## Slide 22: Natural Response Summary
RL Circuit
Inductor current cannot change instantaneously
time constant
RC Circuit
Capacitor voltage cannot change instantaneously
time constant
R
i
L
+
v
–
R
C

## Slide 23: Basic RL and RC Circuits
About Calculation for The Initial Value
iC
iL
i
t=0
+
_
1A

+
-
vL(0+)
vC(0+)=4V
i(0+)
iC(0+)
iL(0+)

## Slide 24: Problem 1
Close the switch, and find I1, I2, I3, Q, and Vc immediately after the switch is closed

## Slide 25: Solution
The capacitor just starts to be charged
⇒ Q= 0.
Vc = Q/C = 0
Req=R1+R2R3/R2+R3
= 14.5kΩ
I1=Ieq=9/Req
≈0.62mA

## Slide 26
V2=V3=I1.(R2R3)/R2+R3
I2=V2/R2 = 0.1 mA
I3 = V3/R3 = 0.52 mA

## Slide 27: Problem 2
After the switch is closed for a length of time sufficiently long for the capacitor to become fully charged, find I1,I2,I3,Q, andVc
I3 = 09 =I1(R1+R2) = 27.I1
I1=I2=9/27=0.33mA
V2 = V3 = 15/3 = 5
Q = C.Vc = 50uC

## Slide 28: Problem 3
The switch is then reopened. Find I1,I2,I3,Q,and
Vc immediately after the switch is reopened
Once the switch is open, the left-hand side circuit is open and therefore I1= 0.
Q = 50uC
Vc=Q/C = 5 V
I2 = I3
Vc=I2R2+I3R3=I2(R2+R3) = 18*I2
I2 = 5/18 = 0.28 mA

## Slide 29: Problem 4
After the switch is reopened for a length of time sufficiently long for the capacitor to become fully discharged, find
I1,I2,I3,Q,and Vc
I1 = 0
Q = Vc = 0 as cap is fully discharged
I2 = I3 = 0

## Slide 30
Second-Order Circuit
A second-order circuit is characterized by a second-order differential equation. It consists of resistors and the equivalent of two energy storage elements.
Typical examples of second-order circuits:
C
R
L
US
+
_
C
US
+
_
L
R
(a) series RLC circuit
(b) parallel RLC circuit