## Slide 1
Multiplexer
A multiplexer is a device which has
(i) number of input lines
(ii) number of selection lines
(iii) only one output line
It steers one of 2n inputs to a single output line, using n selection lines. Also known as a data selector.
2n:1
Multiplexer
output
inputs
select
...

## Slide 2
Multiplexer
Truth table for a 4-to-1 multiplexer:
mux
Y
Inputs
select
S1 S0
I0
I1
I2
I3
4:1
MUX
Y
Inputs
select
S1 S0
I0
I1
I2
I3
0
1
2
3
Output

## Slide 3
Multiplexer
Output of multiplexer is
“sum of the (product of data lines and selection lines)”
Example: the output of a 4-to-1 multiplexer is:
Y = I0.(S1’.S0') + I1.(S1’.S0) + I2.(S1.S0') + I3.(S1.S0)
A 2n-to-1-line multiplexer, or simply 2n:1 MUX, is made from an n: 2n decoder by adding to it 2n input lines, one to each AND gate.

## Slide 4
Multiplexer
S1
S0
I0
I1
I2
I3
Y

## Slide 5
Multiplexer
An application:
Helps share a single communication line among a number of devices.
At any time, only one source and one destination can use the communication line.

## Slide 6
Larger Multiplexers
Larger multiplexers can be constructed from smaller ones.
An 8-to-1 multiplexer can be constructed from smaller multiplexers like this (note placement of selector lines):
4:1 MUX
I0
I1
I2
I3
S1 S0
4:1 MUX
I4
I5
I6
I7
S1 S0
2:1 MUX
S2
Y

## Slide 7
Larger Multiplexers
4:1 MUX
I0
I1
I2
I3
S1 S0
4:1 MUX
I4
I5
I6
I7
S1 S0
2:1 MUX
S2
Y
When
S2S1S0 = 000
I0
I4
I0

## Slide 8
Larger Multiplexers
4:1 MUX
I0
I1
I2
I3
S1 S0
4:1 MUX
I4
I5
I6
I7
S1 S0
2:1 MUX
S2
Y
When
S2S1S0 = 110
I2
I6
I6

## Slide 9
Larger Multiplexers
Another implementation of an 8-to-1 multiplexer using smaller multiplexers:
4:1 MUX
S2 S1
I0
I1
2:1 MUX
S0
I2
I3
2:1 MUX
S0
I4
I5
2:1 MUX
S0
I6
I7
2:1 MUX
S0
I0
When
S2S1S0 = 000
I0
I4
I2
I6

## Slide 10
Larger Multiplexers
4:1 MUX
I0
I1
I2
I3
S1 S0
4:1 MUX
I4
I5
I6
I7
S1 S0
2:1 MUX
S2
Y
When
S2S1S0 = 001

## Slide 11
Larger Multiplexers
A 16-to-1 multiplexer can be constructed from five 4-to-1 multiplexers:

## Slide 12
Multiplexers: Implementing Functions
This method works because:
Output = m0.I0 + m1.I1 + m2.I2 + m3.I3 + m4.I4 + m5.I5 + m6.I6 + m7.I7
Supplying ‘1’ to I1,I3,I5,I6 , and ‘0’ to the rest:
Output = m1 + m3 + m5 + m6
F(A,B,C) = S m(1,3,5,6)
mux
A B C
0
1
2
3
4
5
6
7
0
1
0
1
0
1
1
0
F

## Slide 13
Multiplexers: Implementing Functions
A Boolean function can be implemented using multiplexers.
A 2n-to-1 multiplexer can implement a Boolean function of n input variables, as follows:
  (i) Express in sum-of-minterms form.
Example: F(A,B,C) = A'B'C + A'BC + AB'C + ABC'
= S m(1,3,5,6)
  (ii) Connect n variables to the n selection lines.
  (iii) Put a '1' on a data line if it is a minterm of the function, '0' otherwise.

## Slide 14: Multiplexers: Implementing Functions
This method works because:
Output = m0.I0 + m1.I1 + m2.I2 + m3.I3 + m4.I4 + m5.I5 + m6.I6 + m7.I7
Supplying ‘1’ to I1,I3,I5,I6 , and ‘0’ to the rest:
Output = m1 + m3 + m5 + m6
F(A,B,C) = S m(1,3,5,6)
mux
A B C
0
1
2
3
4
5
6
7
0
1
0
1
0
1
1
0
F

## Slide 15: Multiplexers: Implementing Functions
Example: Use a 74151A to implement:
f(x1,x2,x3) =  m(0,2,3,5)
Realization of f(x1,x2,x3) = m(0,2,3,5).
(a)Truth table.
(b)Implementation with 74151A.

## Slide 16: Using Smaller Multiplexers
Earlier, we saw how a 2n-to-1 multiplexer can be used to implement any Boolean function of n (input) variables.
However, we can use a single smaller 2(n-1)-to-1 multiplexer to implement any Boolean function of n (input) variables.
In particular, the earlier function
F(A,B,C) =  m(1,3,5,6)
can be implemented using a 4-to-1 multiplexer (rather than an 8-to-1 multiplexer).

## Slide 17: Using Smaller Multiplexers
Note: Two of the variables, A, B, are applied as selection lines of the multiplexer, while the inputs of the multiplexer contain 1, C, 0 and C'.
mux
A B C
0
1
2
3
4
5
6
7
1
1
0
1
0
0
1
0
F
mux
A B
0
1
2
3
1
C
0
C'
F
Let’s look at this example:
F(A,B,C) = S m(0,1,3,6) = A’B’C’ + A’B’C + A’BC + ABC’
A’B’

## Slide 18: Using Smaller Multiplexers
Procedure
  1) Express boolean function in “sum-of-minterms” form.
  e.g. F(A,B,C)= S m(0,1,3,6)
  2) Reserve one variable (in our example, we take the least significant one) for input lines of multiplexer, and use the rest for selection lines.
  e.g. C is for input lines, A and B for selection lines.

## Slide 19: Using Smaller Multiplexers
  3) Draw the truth table for function, but grouping inputs by selection line values, and then determine multiplexer inputs by comparing input line (C) and function (F) for corresponding selection line values.
mux
A B
0
1
2
3
1
0
F
C

## Slide 20: Using Smaller Multiplexers
Alternative: What if we use A for input lines, and B, C for selector lines?
A’ (when BC = 00)
A’ (when BC = 01)
A (when BC = 10)
A’ (when BC = 11)
mux
B C
0
1
2
3
A
F

## Slide 21: Using Smaller Multiplexers
Example: Implement using a 74151A the function:
f(x1,x2,x3,x4) =  m(0,1,2,3,4,9,13,14,15)

## Slide 22
Implement the Boolean function by using 8x1 MUX –
F(A,B,C,D)=∑m(0,1,3,4,8,9,14,15)
Total number of variables , n= 4 (A,B,C,D)
Select line variable (n-1) = 3 (B,C,D) Input variable = 1 (A)
 | I0 | I1 | I2 | I3 | I4 | I5 | I6 | I7
(A’)0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
(A)1 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
 | 1 | 1 | 0 | A’ | A’ | 0 | A | A
Implementation table –

## Slide 24: Implement the following function using 4x1 MUX- F(A,B,C,D)=∑m(0,1,3,4,7,8,9,11,14,15)

## Slide 25
Solving minterms corresponding to I0-
I0 C’D’+C’D+CD
=C’(D’+D)+CD
=C’+CD
=C’+D
Solving minterms corresponding to I1-
I1 C’D’+CD = C (X-NOR) D
Solving minterms corresponding to I2-
I2 C’D’+C’D+C = C’+D
Solving minterms corresponding to I3-
I3 CD’+CD = C

## Slide 27
Figure 6.19. A 4-to-1 multiplexer built using a decoder.
w
1
w
0
w
0
En
y
0
w
1
y
1
y
2
y
3
w
2
w
3
f
s
0
s
1
1